## Slide 1
INTEGRATIVE CHALLENGE M4 · E80 GROUP LOGISTICS CASE
Intelligent Multi Agent
AGV Fleet Coordination
BFS routing + Independent Q Learning for battery aware mission assignment
Final Presentation
Team .gitignore

## Slide 2
INTRODUCTION · CASE STUDY
A 4 AGV fleet inside an e80 Group
distribution centre
48 m x 30 m
distribution centre, 1 m occupancy grid
4 AGVs
shared by production lines, racks and truck docks
3 chargers
a scarce, contested resource
Stochastic shift
orders, pedestrians and aisle closures arrive over time
SIMPLIFIED FLOOR PLAN
Production
Storage racks
Truck docks
Chargers (x3)
02

## Slide 3
INTRODUCTION · PROBLEM STATEMENT
The baseline rule based fleet fails
in three linked ways
AGVs strand themselves
Battery is checked only while Available, at a fixed 45% threshold. 3.55 run flat events per 400 tick shift, each a 25 tick tow.
3.55
run flats / shift
Charging is all or nothing
An AGV charges only once it drops below threshold, then always to 100%, occupying one of only 3 chargers for a long block.
3
chargers, shared
Bids ignore reachability
The bid mixes distance, battery and workload with hand picked weights. Nothing asks: after this mission, can I reach a charger?
w_d, w_b, w_l
chosen by hand
All three are the same underlying issue: a decision whose cost is paid much later, in an environment shaped by three other independent agents.
03

## Slide 4
INTRODUCTION · OBJECTIVES
The question we set out to answer
“Does the proposed intelligent strategy improve the performance of the Multi Agent System?”
01
Diagnose
Measure the baseline's failures rather than assume them (Section 12).
02
Design
Replace the fixed threshold rule with a learned, state aware policy.
03
Verify
Test both strategies under byte identical conditions, on unseen scenarios.
04
Report
Show gains and tradeoffs together, not just the metrics that improved.
04

## Slide 5
METHODOLOGY · ARCHITECTURE
Two layers, two questions
BFS answers “how do I get there?” · Q Learning answers “what should I decide?”
Perception
Position, battery, pending missions, chargers, pedestrians
State
Compressed to (battery, distance, backlog, reserve, parked)
Q Learning
decision
arg max Q(s,a) over 4 legal actions
BFS routing
Shortest 4 connected path to the chosen target
Why BFS, not A* / Dijkstra: a 4 connected grid with uniform 1 m edge cost and 865 traversable cells; uniform cost Dijkstra degenerates into BFS, and A* only adds heuristic overhead.
05

## Slide 6
METHODOLOGY · THE LEARNED POLICY
State, actions and reward
STATE · 288 possible states
Battery
own charge bucket
4
Distance
BFS route to closest mission
4
Backlog
pending missions
3
Reserve
charge left after full round trip
3
Parked
on a charger?
2
The reserve feature ties BFS to the decision: charge left over after pickup → drop off → nearest charger. Negative reserve means this mission strands the AGV.
ACTIONS
BID_NEAREST
BID_PRIORITY
WAIT
GO_CHARGE
SEMI MDP REWARD
r = R_done · Δcompleted − c_tΔt − c_dΔcells − P_strand·Δflat − c_idleΔt·1[WAIT & backlog]
Evaluated only when the AGV returns to a decision point, so delayed consequences are charged to the decision that caused them.
WHY THE DISCOUNT MATTERS
γ = 0.999 per tick, not the usual 0.99. At γ = 0.99, a 60 tick mission's continuation value is multiplied by 0.99⁶⁰ ≈ 0.55, while a 1 tick WAIT keeps 0.99 of it; the policy learns to idle.
06

## Slide 7
METHODOLOGY · COORDINATION
How the fleet communicates and negotiates
Communication
Mission Manager broadcasts every pending mission to all AGVs, once per tick.
Each AGV replies with a bid U_i,k that implicitly reveals its own battery and workload.
Positions are shared implicitly through the occupancy grid the movement arbiter reads.
Negotiation & collaboration
Every mission goes to the highest bidder; the manager only reports the argmax.
A mission leaves the pool the instant it's accepted; no two AGVs chase the same job.
A carrier that runs flat releases its mission back to the pool for someone else.
Bid utility (identical in both strategies): U_i,k = −w_d D_i,k + w_b B_i − w_l L_i
07

## Slide 8
METHODOLOGY · COORDINATION PARADIGM
Centralized control vs. independent agents
DECENTRALIZED (CHOSEN)
Each AGV keeps its own 288 state Q table, updated only from its own experience: no shared parameters, no central critic.
AGV 1
Q table
AGV 2
Q table
AGV 3
Q table
AGV 4
Q table
Cost: nonstationarity, while AGV 1 learns, AGV 2's behaviour keeps changing underneath it, which is the honest multi agent setting (agents are autonomous, not one controller in four bodies).
CENTRALIZED CONTROL (NOT USED)
A single joint policy over the fleet needs 288⁴ ≈ 6.88 billion states, against 288 per agent kept independent: out of reach for tabular Q learning.
One controller ingesting the full fleet state every tick becomes a communication bottleneck and a single point of failure: the opposite of this fleet's auction design.
A 5th AGV would multiply the joint state space by another 288×; an independent table instead just adds one more compact 1,152 entry table.
08

## Slide 9
METHODOLOGY · EXPERIMENTAL DESIGN
Decentralized learning, tested fairly
INDEPENDENT Q LEARNING
Each AGV owns a separate Q table, updated only from its own experience: no shared parameters, no central critic.
AGV 1
Q table
AGV 2
Q table
AGV 3
Q table
AGV 4
Q table
Cost: nonstationarity, while AGV 1 learns, AGV 2's behaviour keeps changing underneath it, which is the honest multi agent setting (agents are autonomous, not one controller in four bodies).
A FAIR BASELINE VS PROPOSED TEST
Entire world timeline pregenerated from the scenario seed (orders, pedestrians, closures, initial batteries) before either strategy runs.
Reverified field by field on 10 seeds: order streams, per tick pedestrian positions, closed cells, initial batteries, 0 / 10 differing worlds.
Training seeds (10000+) are disjoint from the 20 evaluation seeds (0 to 19): results measure generalisation, not memorisation.
09

## Slide 10
Independent Q-Learning Converges Over Training
Moving average across 1,000 training episodes (window = 40)
↑
~3.6 → ~4.8
Throughput
Missions completed per 100 ticks steadily rises as the policy learns.
↓
~13 → ~2
Run-flat events
Battery-stranding incidents per episode drop as charging timing improves.
↓
1.0 → 0.05
Exploration rate ε
Decays toward a near-greedy policy as the agents stop exploring.

## Slide 11
RESULTS · 20 PAIRED EVALUATION SHIFTS
Yes, on throughput, mission time, distance
and run flat events
Chart: 
| Missions completed | Cycle time (ticks) | Distance / mission | Run flats / shift
Baseline | 16.15 | 142.75 | 85.43 | 3.45
Proposed (Q Learning) | 20.7 | 95.8 | 66.95 | 1.35
+28.2%
throughput
−32.9%
cycle time
−60.9%
run flat events
−21.6%
distance / mission
Paired seeds won: 15 to 20 / 20 across the four metrics above.
10

## Slide 12
RESULTS · THE HONEST PICTURE
The gains come with two measured
tradeoffs
− Utilisation
69.05% → 66.22%
−4.1%, only 6/20 seeds won
The fleet is busy less often, because it is doing less useless driving, not less useful work. Utilisation measures how busy the fleet is, not how much it delivers.
+ Replanning
63.4 → 75.3 BFS replans
+18.8%, only 9/20 seeds won
The learned policy keeps AGVs circulating more, so they meet each other, pedestrians and closures more often: real compute/communication cost this sim doesn't charge for.
WHAT THE POLICY LEARNED
Battery 25 to 50%, work pending, reserve negative → GO_CHARGE (decline the mission that would strand it; this single rule drives most of the run flat reduction)
Parked, battery ≥75%, reserve comfortable → leaves early instead of always waiting for 100% · Idle with empty queue → opportunistic top up
11

## Slide 13
CONCLUSIONS
It works, and we know exactly where
it still falls short
Yes, on the metrics the proposal set out to change, measured on 20 unseen paired scenarios, under verified byte identical conditions, with the metrics that worsened reported alongside the ones that improved.
REMAINING LIMITATIONS
Coarse 288 state grid; battery cutoffs at 25/50/75% are arbitrary.
AGVs pick a mission type, not a specific mission; the auction resolves the rest.
Independent learning is nonstationary by construction; convergence stays noisy.
No mid mission retasking, even if a much better mission appears.
NEXT STEPS
1
Bid on a specific mission via function approximation (DQN).
2
Solve each round's assignment jointly with the Hungarian algorithm.
3
Time window route reservations to deconflict before AGVs meet.
4
Tune bid weights by search; allow charger reservation and retasking.
12

## Slide 14
Thank you
Questions & discussion
REFERENCES & TOOLS
Watkins, C.J.C.H. & Dayan, P. (1992). Q Learning. Machine Learning, 8, 279 to 292.
Sutton, R.S. & Barto, A.G. (2018). Reinforcement Learning: An Introduction (2nd ed.), MIT Press.
AgentPy documentation: agent based modelling framework used for the simulation.
Integrative Challenge M3 baseline implementation: e80 Group logistics scenario.
13